NextOS API (Updated 18 Jan 2018)

This document describes the NextOS API, which directly descends from the +3DOS API present in the Sinclair ZX Spectrum +2A/+2B/+3 and the IDEDOS API additionally provided with the ZX Spectrum +3e ROMs.

It also describes the provided esxDOS-compatible API, which is compatible with esxDOS 0.8.x, but contains several enhancements.

This should be read in conjunction with the other documents:
NextBASIC file-related commands and features
NextBASIC new commands and features
NextOS Editor features
NextOS Unimplemented features

A list of updates made to this document is now provided at the end.

Available APIs

NextOS provides 2 distinct and separate APIs:
- a +3DOS-compatible API, providing the main NextOS API
- an esxDOS-compatible API, providing file-based calls for SD card access

The +3DOS-compatible API descends directly from the original +3DOS, provided with the Sinclair ZX Spectrum +3/+2A/+2B.

The esxDOS-compatible API is provided by a thin layer on top of +3DOS, and is compatible with esxDOS 0.8.x, with some additional facilities such as support for long filenames (LFNs), wildcards in filenames and a low-overhead file streaming facility.

Both APIs provide general file-access calls. The esxDOS-compatible API is generally easier to use, but lacks the ability to access files on filesystems which are not FAT16/32 (such as the RAMdisk, and mounted CP/M and +3 disk images). It also lacks some of the more advanced features of the +3DOS-compatible API, such as bank allocation, BASIC command execution and file-browser dialogs.

The +3DOS-compatible API is described in the first section of the following pages, with the esxDOS-compatible API described in second section.

IMPORTANT NOTE:

When calling either the +3DOS-compatible or esxDOS-compatible API, make sure you have not left layer 2 writes enabled (ie bit 0 of port $123b should be zero when making any API call).

This is important because if layer 2 writes are left enabled, they can interfere with the operation of the system calls, which page in DivMMC RAM to the same region of memory ($0000-$3fff).

It is perfectly okay to leave layer 2 turned on and displayed (with bit 1 of port $123b) during API calls; only the writes need to be disabled.
The +3DOS-compatible API

The +3DOS-compatible API provides most of the facilities available on both the original +3/+2A/+2B, and the later +3e ROMs, with many additional facilities specific to the Next.

To make a +3DOS API call, you must first ensure that the memory bank configuration is set up correctly (with ROM 2 selected at the bottom of memory, RAM bank 7 at the top of memory and the stack located below $BFE0).

Once this is done, call the address indicated in the API call. You then probably want to restore the memory configuration to normal (with ROM 3 selected at the bottom of memory, and RAM bank 0 at the top of memory).

Please note that a few calls require the memory configuration to be slightly different on entry (with RAM bank 0 at the top of memory); this is noted in the individual documentation for those calls, which are generally BASIC-releated (eg IDE_STREAM_* and IDE_BASIC).

Useful example code showing how to use the API is available in the original +3 manual (section “Calling +3DOS from BASIC”), online here:

http://www.worldofspectrum.org/ZXSpectrum128+3Manual/chapter8pt26.html

This document does not describe unchanged calls, which are available in these online documents:

http://www.worldofspectrum.org/ZXSpectrum128+3Manual/chapter8pt27.html
http://www.worldofspectrum.org/zxplus3e/idedos.html

The following filesystem-related API calls are provided (*=effects have changed since originally documented in +3 manual or on +3e website; %=new for NextOS):

DOS_VERSION ($0103)	Get +3DOS issue and version numbers
*DOS_OPEN ($0106)	Create and/or open a file
DOS_CLOSE ($0109)	Close a file
DOS_ABANDON ($010C)	Abandon a file
DOS_REF_HEAD ($010F)	Point at the header data for this file
DOS_READ ($0112)	Read bytes into memory
DOS_WRITE ($0115)	Write bytes from memory
DOS_BYTE_READ ($0118)	Read a byte
DOS_BYTE_WRITE ($011B)	Write a byte
*DOS_CATALOG ($011E)	Catalog disk directory
*DOS_FREE_SPACE ($0121)	Free space on disk
DOS_DELETE ($0124)	Delete a file
DOS_RENAME ($0127)	Rename a file
DOS_BOOT ($012A)	Boot an operating system or other program
DOS_SET_DRIVE ($012D)	Set/get default drive
DOS_SET_USER ($0130)	Set/get default user number
*DOS_GET_POSITION ($0133)	Get file pointer for random access
DOS_SET_POSITION ($0136)	Set file pointer for random access
*DOS_GET_EOF ($0139)	Get end of file position for random access
DOS_GET_1346 ($013C)	Get memory usage in pages 1, 3, 4, 6
DOS_SET_1346 ($013F)	Re-allocate memory usage in pages 1, 3, 4, 6
DOS_FLUSH ($0142)	Bring disk up to date
DOS_SET_ACCESS ($0145)	Change open file's access mode
DOS_SET_ATTRIBUTES ($0148)	Change a file's attributes
DOS_SET_MESSAGE ($014E)	Enable/disable error messages

IDE_VERSION ($00A0)	Get IDEDOS version number
IDE_SWAP_OPEN ($00D9)	Open a swap partition
IDE_SWAP_CLOSE ($00DC)	Close a swap partition
IDE_SWAP_OUT ($00DF)	Write block to swap partition
IDE_SWAP_IN ($00E2)	Read block from swap partition
IDE_SWAP_EX ($00E5)	Exchange block with swap partition
IDE_SWAP_POS ($00E8)	Get current block number in swap partition
IDE_SWAP_MOVE ($00EB)	Set current block number in swap partition
IDE_SWAP_RESIZE ($00EE)	Change block size of swap partition
IDE_PARTITION_FIND ($00B5)	Find named partition
*IDE_DOS_MAP ($00F1)	Map drive to partition
*IDE_DOS_UNMAP ($00F4)	Unmap drive
IDE_DOS_MAPPING ($00F7)	Get drive mapping
*IDE_SNAPLOAD ($00FD)	Load a snapshot
*IDE_PATH ($01b1)	Create, delete, change or get directory
%IDE_CAPACITY ($01b4)	Get card capacity
%IDE_GET_LFN ($01b7)	Get long filename
%IDE_BROWSER ($01ba)	File browser

The following non-filesystem-related API calls are provided:

IDE_STREAM_OPEN ($0056)	Open stream to a channel
IDE_STREAM_CLOSE ($0059)	Close stream and attached channel
IDE_STREAM_IN ($005c)	Get byte from current stream
IDE_STREAM_OUT ($005f)	Write byte to current stream
IDE_STREAM_PTR ($0062)	Get or set pointer information for current stream
%IDE_BANK ($01bd)	Allocate or free 8K banks in ZX or DivMMC memory
%IDE_BASIC ($01c0)	Execute a BASIC command line
%IDE_WINDOW_LINEIN ($01c3)	Input line from current window stream
%IDE_WINDOW_STRING ($01c6)	Output string to current window stream
%IDE_INTEGER_VAR ($01c9)	Get or set NextBASIC integer variable
%IDE_RTC ($01cc)	Query the real-time-clock module

The following API calls are related to floppy drives and will not be useful for most software (included for legacy software use only):

DOS_REF_XDPB ($0151)	Point at XDPB for low level disk access
DOS_MAP_B ($0154)	Map B: onto unit 0 or 1
DD_INTERFACE ($0157)	Is the floppy disk driver interface present?
DD_INIT ($015A)	Initialise disk driver
DD_SETUP ($015D)	Specify drive parameters
DD_SET_RETRY ($0160)	Set try/retry count
DD_READ_SECTOR ($0163)	Read a sector
DD_WRITE_SECTOR ($0166)	Write a sector
DD_CHECK_SECTOR ($0169)	Check a sector
DD_FORMAT ($016C)	Format a track
DD_READ_ID ($016F)	Read a sector identifier
DD_TEST_UNSUITABLE ($0172)	Test media suitability
DD_LOGIN ($0175)	Log in disk, initialise XDPB
DD_SEL_FORMAT ($0178)	Pre-initialise XDPB for DD FORMAT
DD_ASK_1 ($017B)	Is unit 1 (external drive) present?
DD_DRIVE_STATUS ($017E)	Fetch drive status
DD_EQUIPMENT ($0181)	What type of drive?
DD_ENCODE ($0184)	Set intercept routine for copy protection
DD_L_XDPB ($0187)	Initialise an XDPB from a disk specification
DD_L_DPB ($018A)	Initialise a DPB from a disk specification
DD_L_SEEK ($018D)	uPD765A seek driver
DD_L_READ ($0190)	uPD765A read driver
DD_L_WRITE ($0193)	uPD765A write driver
DD_L_ON_MOTOR ($0196)	Motor on, wait for motor-on time
DD_L_T_OFF_MOTOR ($0199)	Start the motor-off ticker
DD_L_OFF_MOTOR ($019C)	Turn the motor off

The following API calls are present but generally for system use only and not useful for games/applications:

DOS_INITIALISE ($0100)	Initialise +3DOS
IDE_INTERFACE ($00A3)	Initialise card interfaces
IDE_INIT ($00A6)	Initialise IDEDOS
IDE_DRIVE ($00A9)	Get unit handle
*IDE_SECTOR_READ ($00AC)	Low-level sector read
*IDE_SECTOR_WRITE ($00AF)	Low-level sector write
*IDE_PARTITION_NEW ($00B8)	Create partition
*IDE_PARTITION_INIT ($00BB)	Initialise partition
IDE_PARTITON_READ ($00C4)	Read a partition entry
IDE_PARTITION_OPEN ($00CD)	Open a partition
IDE_PARTITION_CLOSE ($00D0)	Close a partition
IDE_PARTITIONS ($01a5)	Get number of open partitions

The following API calls were previously available in +3DOS/IDEDOS but are now deprecated and will return an error of rc_notimp:

DOS_OPEN_DRIVE ($014B)	Open a drive as a single file
IDE_FORMAT ($00B2)	Format a partition
IDE_PARTITION_ERASE ($00BE)	Delete a partition
IDE_PARTITION_RENAME ($00C1)	Rename a partition
IDE_PARTITION_WRITE ($00C7)	Write a partition entry
IDE_PARTITION_WINFO ($00CA)	Write type-specific partition information
IDE_PARTITION_GETINFO ($00D3)	Get byte from type-specific partition information
IDE_PARTITION_SETINFO ($00D6)	Set byte in type-specific partition information
IDE_DOS_UNPERMANENT ($00FA)	Remove permanent drive mapping
IDE_IDENTIFY ($01a2)	Return IDE drive identity information

Updated calls

The following calls have new/updated features, which are highlighted in GREEN. (Some changes are due to removed parameters which are not shown). NOTE: Calls for internal use only have not yet been included here.

It should additionally be noted that the IDE_STREAM_* calls may corrupt the alternate register set, in addition to the effects on the standard register set noted for each individual call.

As well as describing additional features, DOS_CATALOG contains additional text which clarifies points that are not obvious from the documentation in the original +3 manual.

DOS_OPEN
0106h (262)

Create and/or open a file

There is a choice of action depending on whether or not the file
already exists. The choices are 'open action' or 'create action', and
are specified in DE. If the file already exists, then the open action
is followed; otherwise the create action is followed.

Open action

        0. Error - File already exists.

        1. Open the file, read the header (if any). Position file
        pointer after header.

        2. Open the file, ignore any header. Position file pointer at
        000000h (0).

        3. Assume given filename is 'filename.type'. Erase
        'filename.BAK' (if it exists). Rename 'filename.type' to
        'filename.BAK'. Follow create action.

        4. Erase existing version. Follow create action.

Create action

        0. Error - File does not exist.

        1. Create and open new file with a header. Position file
        pointer after header.

        2. Create and open new file without a header. Position file
        pointer at 000000h (0).

(Example: To simulate the tape action of... 'if the file exists open
it, otherwise create it with a header', set open action = 1, create
action = 1.)

(Example: To open a file and report an error if it does not exist, set
open action = 1, create action = 0.)

(Example: To create a new file with a header, first renaming any
existing version to '.BAK', set open action = 3, create action = 1.)

Files with headers have their EOF position recorded as the smallest
byte position greater than all written byte positions.

Files without headers have their EOF position recorded as the byte at
the start of the smallest 128 byte record position greater than all
written record positions.

Soft-EOF is the character 1Ah (26) and is nothing to do with the EOF
position, only the routine DOS BYTE READ knows about soft-EOF.

The header data area is 8 bytes long and may be used by the caller for
any purpose whatsoever. If open action = 1, and the file exists (and
has a header), then the header data is read from the file, otherwise
the header data is zeroised. The header data is available even if the
file does not have a header. Call DOS REF HEAD to access the header
data.

Note that +3 BASIC makes use of the first 7 of these 8 bytes as
follows:

+---------------+-------+-------+-------+-------+-------+-------+-------+
| BYTE | 0 | 1 | 2 | 3 | 4 | 5 | 6 |
+---------------+-------+-------+-------+-------+-------+-------+-------+
| Program 0 file length 8000h or LINE offset to prog |
| Numeric array 1 file length xxx name xxx xxx |
| Character array 2 file length xxx name xxx xxx |
| CODE or SCREEN$ 3 file length load address xxx xxx |
+-----------------------------------------------------------------------+

(xxx = doesn't matter)

If creating a file that will subsequently be LOADed within BASIC, then
these bytes should be filled with the relevant values.

If the file is opened with exclusive-write or exclusive-read-write
access (and the file has a header), then the header is updated when
the file is closed.

A file that is already open for shared-read access on another file
number may only be opened for shared-read access on this file number.

A file that is already open for exclusive-read or exclusive-write or
exclusive-read-write access on another file number may not be opened
on this file number.

If the open action is 1 or 2 and the create action is 0 (ie only an existing file is to be opened) then the filename may optionally contain the wildcard characters * and ?. In this case, the first file that matches the wildcard will be opened.

ENTRY CONDITIONS
        B = File number 0...15
        C = Access mode required
        Bits 0...2 values:
        1 = exclusive-read
        2 = exclusive-write
        3 = exclusive-read-write
        5 = shared-read
        Bits 3...7 = 0 (reserved)
        D = Create action
        E = Open action
        HL = Address of filename (no wildcards, unless D=0 and E=1 or 2)

EXIT CONDITIONS
        If file newly created:
        Carry true
        Zero true
        A corrupt
        If existing file opened:
        Carry true
        Zero false
        A corrupt
        Otherwise:
        Carry false
        A = Error code
        Always:
        BC DE HL IX corrupt
        All other registers preserved

DOS_CATALOG
011Eh (286)

Fills a buffer with part of the directory.

The filename optionally specifies the drive, path, user and a (possibly ambiguous) filename (which may contain wildcard characters ? and *).

Since the size of a directory is variable (and may be quite large),
this routine permits the directory to be catalogued in a number of
small sections. The caller passes a buffer pre-loaded with the first
required filename, or zeroes for the start of the directory. The
buffer is loaded with part (or all, if it fits) of the directory
sorted in ASCII order. If more of the directory is required, this
routine is re-called with the buffer re-initialised with the last file
previously returned. This procedure is followed repeatedly until all
of the directory has been catalogued.

Note that +3DOS format disks (which are the same as single-sided,
single track AMSTRAD PCW range format disks) may have a maximum of 64
directory entries.

Buffer format:

        Entry 0
        Entry 1
        Entry 2
        Entry 3
        ...to...
        Entry n

Entry 0 must be preloaded with the first 'filename.type'
required. Entry 1 will contain the first matching filename greater
than the preloaded entry (if any). A zeroised preload entry is OK.

If the buffer is too small for the directory, this routine can be
called again with entry 0 replaced by entry n to fetch the next part
of the directory.

Entry format (13 bytes long):

        Bytes 0...7 - Filename (ASCII) left justified, space
        filled
        Bytes 6...10 - Type (ASCII) left justified, space filledd
        Bytes 11...12 - Size in kilobytes (binary)

Any of the filename or extension characters may have bit 7 set, as described in the section on file attributes, so these should be masked off if not required.

The file size is the amount of disk space allocated to the file, not
necessarily the same as the amount used by the file.

ENTRY CONDITIONS
        B = n+1, size of buffer in entries, >=2
        C = Filter (if bit is set)
        bit 0 = include system files
   bit 1 = set bit 7 of f7 (the 7th character in the filename) if	the entry has a valid LFN (long filename) which can be
obtained with the IDE_GET_LFN call
   bit 2 = include directories, and set bit 7 of f8 (the 8th
character in the filename) if the entry is a directory
        bits 3...7 = 0 (reserved)
        DE = Address of buffer (first entry initialised)
        HL = Address of filename (wildcards permitted)

EXIT CONDITIONS
        If OK:
        Carry true
        A corrupt
        B = Number of completed entries in buffer, 0...n.
        (If B = n, there may be more to come).
   HL = Directory handle, required to obtain long filenames
  with IDE_GET_LFN

        Otherwise:
        Carry false
        A = Error code
        B HL corrupt
        Always:
        C DE HL IX corrupt
        All other registers preserved

DOS_FREE_SPACE
0121h (289)

How much free space is there on this drive?

ENTRY CONDITIONS
        A = Drive, ASCII 'A'...'P'

EXIT CONDITIONS
        If OK:
        Carry true
        A corrupt
        HL = Free space (in kilobytes, clamped to maximum 65535K)
   BCDE = Free space (in kilobytes)

        Otherwise:
        Carry false
        A = Error code
        HL corrupt
        Always:
        BC DE IX corrupt
        All other registers preserved

DOS_GET_POSITION
0133h (307)

Get the file pointer.

ENTRY CONDITIONS
        B = File number

EXIT CONDITIONS
        If OK:
        Carry true
        A corrupt
        DEHL = File pointer
        (D holds most significant byte; L holds least
        significant byte)
        Otherwise:
        Carry false
        A = Error code
        DE HL corrupt
        Always:
        BC IX corrupt
        All other registers preserved

DOS_GET_EOF
0139h (313)

Get the end of file (EOF) file position greater than all written byte
positions.

Does not affect the file pointer.

Does not consider soft-EOF.

ENTRY CONDITIONS
        B = File number

EXIT CONDITIONS
        If OK:
        Carry true
        A corrupt
        DEHL = File pointer
        (D holds most significant byte; L holds least
        significant byte)
        Otherwise:
        Carry false
        A = Error code
        DE HL corrupt
        Always:
        BC IX corrupt
        All other registers preserved

IDE_DOS_MAP ($00F1)

Map a drive to the specified partition or physical device

IN: A=unit (0 or 1), or physical device:
        2=floppy device 0
        3=floppy device 1
        4=RAMdisk
     BC=partition number
     L=drive letter 'A' to 'P' (uppercase)

OUT(s): Fc=1
OUT(f): Fc=0, A=error code

Register status on return:
......../IX same
AFBCDEHL/.. different

IDE_DOS_UNMAP ($00F4)

Remove mapping from the specified drive

IN: L=drive letter 'A' to 'P' (uppercase)

OUT(s): Fc=1
OUT(f): Fc=0, A=error code

Register status on return:
......../IX same
AFBCDEHL/.. different

IDE_SNAPLOAD ($00FD)

Load a snapshot

IN: HL=filespec, terminated with $ff

OUT(s): Does not return if successful
OUT(f): Fc=0, A=error code

Register status on return:
......../.. same
AFBCDEHL/IX different

Loads and runs a supported snapshot file (files with extension .Z80, .SNA, .O and .P are supported, with others potentially supported in future).

IDE_PATH ($01b1)

IN: A=reason code,
rc_path_change (0),
      rc_path_get (1),
      rc_path_make (2),
      rc_path_delete (3)

    HL=address of pathspec (terminated with $ff)
       NB: For rc_path_get, this must also be a 256-byte buffer
        into which the returned path will be written

OUT(s): Fc=1
OUT(f): Fc=0, A=error code

Register status on return:
......../.... same
AFBCDEHL/IXIY different

This call allows the current directory or path for a particular drive (and user area) to be changed or obtained. It also allows creation and deletion of directories.

For rc_path_change, rc_path_make and rc_path_delete, HL points to a directory specification, terminated by $ff. This may optionally include a drive letter, user area and full path (if not, the current default values are used). For rc_path_change, the current path on that drive is changed to the directory or path specified. For rc_path_make and rc_path_delete, the named directory is created or deleted.

For rc_path_get, HL points to a location specification (ie a drive and/or user area, terminated with a colon and $ff). The current path for that location will then be written to the buffer at HL and terminated with $ff.

Note that this call will return an error of rc_notimp if the drive on which it is operating is formatted with a filesystem that does not support directories (eg a +3DOS floppy drive or RAMdisk).

New calls

The following calls are new for NextOS.

IDE_CAPACITY ($01b4)

Get card capacity

IN: C=unit (0 or 1)

OUT(s): Fc=1
  DEHL=total card capacity in 512-byte sectors
OUT(f): Fc=0, A=error code

Register status on return:
......../.. same
AFBCDEHL/IX different

IDE_GET_LFN ($01b7)

Obtain a long filename and other file information

IN: HL=address of filespec provided to the last DOS_CATALOG call
    IX=directory handle returned by the last DOS_CATALOG call
    DE=address of a file entry within buffer filled by the last DOS_CATALOG call
    BC=address of a 261-byte buffer to receive the long filename

OUT(s): Fc=1
        Buffer at BC is filled with the long filename for the requested entry,
  terminated with $ff. If no long filename was available, the buffer will
        contain the properly-formatted short filename instead.
  BC=date (in MS-DOS format)
  DE=time (in MS-DOS format)
  HLIX=filesize (in bytes)
OUT(f): Fc=0, A=error code

Register status on return:
......../.. same
AFBCDEHL/IX different

This call allows a long filename (or properly-formatted short filename) for an entry in the buffer returned by DOS_CATALOG to be obtained. It also returns additional directory entry details (date, time, file size).

NOTE: No other +3DOS calls should be made between the DOS_CATALOG call and the (multiple) IDE_GET_LFN calls used to obtain the long filenames.

NOTE: If the file entry is a directory, the filesize returned in HLIX will be zero.

IDE_BROWSER ($01ba)

Run the file browser

IN: HL=address of supported filetypes buffer, laid out as follows:
        +0 (1 byte) Length of next entry, n
        +1 (n bytes) 1-3 byte extension, colon, optional BASIC command(s)
        If n=$ff there are no further entries.
     DE=address of $ff-terminated help text for 2 lines at bottom of screen
     A=browser capabilities mask, made by ORing together any of:
        $01, BROWSERCAPS_COPY - files may be copied
        $02, BROWSERCAPS_RENAME - files/dirs may be renamed
        $04, BROWSERCAPS_MKDIR - directories may be created
        $08, BROWSERCAPS_ERASE - files/dirs may be erased
        $10, BROWSERCAPS_REMOUNT- SD card may be remounted
        $80, BROWSERCAPS_SYSCFG - system use only - use browser.cfg
     Alternatively just use one of the two special values:
        $00, BROWSERCAPS_NONE - no special capabilities
        $1f, BROWSERCAPS_ALL - all capabilities enabled

OUT(s): Fc=1
        If Fz=1, ENTER was pressed with a filetype that is present in the
        filetype buffer, and:
        HL=address of short filename (terminated with $ff) in RAM 7
        If Fz=0, SPACE/BREAK was pressed
OUT(f): Fc=0, A=error

Register status on return:
......../.. same
AFBCDEHL/IX different

NOTES:

The help text can contain any standard full-screen mode window control codes, but if the character size is changed, it should be changed back to size 5 at the end.

It is intended that applications wishing to use the Browser as a “save file” dialog should direct the user to navigate to the correct drive/directory and press SPACE. At this point the call will exit with the current drive and directory set as the user selected and Fz=0 to indicate SPACE was pressed. Since the screen is not cleared on exit, the application can then request input of the filename on the bottom two lines of the screen, giving a seamless user experience.

Call does not return if a supported filetype was selected which had anything following the colon in the filetype buffer. In this case, the additional data is treated as plain text, then tokenized and executed as a BASIC command. NOTE: No terminator should be added to the end of the command.

The ? character may be used as a wildcard to match a single character in the filetype.

The * character may be used as a wildcard to match remaining characters in the filetype.

Most applications will not want a BASIC command to be executed and so should provide a simple list of all the filetypes that they want to be selectable.

Example filetype buffer contents:
defb	4	; length of first entry
defm	“XYZ:”	; match this filetype and return to caller with it
defb	12	; length of second entry
defm	“X:.hexdump |”	; match this filetype and execute .hexdump on it
defb	3	; length of third entry
defm	“Z?:”	; matches .z3, .z4, .z5 etc
defb	3	; length of fourth entry
defm	“Z*:”	; matches .z, .zip etc
defb	$ff	; table terminator

To match all files, you can provide a simple table like this:
defb	2
defm	“*:”
defb	$ff

IDE_BANK ($01bd)

Allocate or free 8K RAM banks in main ZX memory or DivMMC memory

IN: H=bank type:
        rc_banktype_zx (0), ZX memory half-banks (8K size)
        rc_banktype_mmc (1), DivMMC memory banks (8K size)
     L=reason:
 rc_bank_total (0), return total number of 8K banks of specified type
 rc_bank_alloc (1), allocate next available 8K bank
 rc_bank_reserve (2), reserve bank specified in E (0..total-1)
 rc_bank_free (3), free bank specified in E (0..total-1)
     E=8K bank ID (0..total-1), for rc_bank_reserve/rc_bank_free

OUT(s): Fc=1
        E=8K bank ID (0..total-1), for rc_bank_alloc
        E=total number of 8K banks of specified type, for rc_bank_total

OUT(f): Fc=0
        A=error: rc_inuse if no available banks to allocate
        rc_badparam if H, L or E is invalid

Register status on return:
......../.. same
AFBCDEHL/IX different

NOTE:

This call is provided for applications that wish to co-exist with other applications, dot commands and BASIC programs without overwriting each other's memory.

Bank IDs are for 8K half-banks, numbered from 0 upwards. For ZX memory they can be paged using the MMU instructions.

NextOS/NextBASIC normally reserves the first 18 x 8K banks of ZX memory for its own use, and the first 6 x 8K banks of DivMMC memory. However, BASIC programs or TSR machine code programs could also reserve memory before your program is loaded, so it is usually easier to allocate using rc_bank_alloc rather than rc_bank_reserve.

NextOS/NextBASIC also owns the layer 2 banks (normally 16K banks 9,10,11: 8K banks 18-23, but may have been changed by the LAYER BANK command). However, you can use such banks if you are in control of the system and not using layer 2: the current layer 2 banks can be found by reading Next registers $12 and $13 to find the base of the current front and back buffers, respectively.

Take care to free any banks you allocate before exiting, otherwise they will be unavailable to the user until after a reset. A NEW command *does not* free reserved banks back into the system.

IDE_BASIC ($01c0)

Execute a BASIC command line

IN: HL=address of tokenized BASIC command line, terminated with $0d

OUT(s): Fc=1
        System variable ERR_NR contains generated BASIC error code-1
  ($ff means BASIC command completed successfully)

Register status on return:
......../.. same
AFBCDEHL/IX different

NOTES:

This call must be made with the ROM2/RAM5/RAM2/RAM0 memory configuration rather than the usual +3DOS configuration. The stack must be located between STKEND and RAMTOP (the normal location for the stack during BASIC operation).

Any number of BASIC commands may be executed, separated by colons (:), and the line must be terminated with an ENTER character ($0d).

This call may be particularly useful for setting particular screen modes with the LAYER command, which will ensure that the system variables are correctly set up for printing to windows or the main screen in the selected mode.

IDE_WINDOW_LINEIN ($01c3)

Input line from current window stream

IN: required window has been made current via ROM 3 / $1601
     HL=buffer address (must lie entirely below $c000)
     A=buffer size (1..255 bytes)
     E=number of characters already in the input buffer (0 for an entirely new
       input). Must be less than A.

OUT: E=number of characters returned in input buffer

Register status on return:
......../.. same
AFBCDEHL/IX different

NOTES:

This call invokes the window line input handler, allowing the user to enter new characters and edit the input with the cursor keys and delete.

The input buffer can be primed with an initial string for the user to edit. If this is the case, E should be set to the number of characters in the initial string (otherwise, set E=0).

+3 BASIC errors may be invoked

IDE_WINDOW_STRING ($01c6)

Output string to current window stream

IN: required window has been made current via ROM 3 / $1601
     HL=address of string (must lie entirely below $c000)
     E=string termination condition:
       if E=$ff, string is terminated with a $ff character
       if E=$80, last character in the string has bit 7 set
       if E<$80, E=number of characters in the string (may be
        terminated earlier with $ff)
OUT: -

Register status on return:
......../.. same
AFBCDEHL/IX different

NOTES:

This call is intended for efficient outputting of strings to window channels, avoiding the significant per-character overhead associated with outputting each individual character via RST $10 or IDE_STREAM_OUT.

+3 BASIC errors may be invoked

IDE_INTEGER_VAR ($01c9)

Get or set NextBASIC integer variable

IN: B=0 for standard variable, B=1 for array
     C=variable number (0=A,1=B...25=Z)
     L=array index (0..63) if B=1
     H=0 to get variable, 1 to set variable
     DE=value (if H=1)

OUT(s): Fc=1
        DE=value (if H=0)

OUT(f): Fc=0
        A=error: rc_badparam if H, L or E is invalid

Register status on return:
......../.. same
AFBCDEHL/IX different

NOTE:

This call provides a convenient interface to pass values between BASIC and machine-code processes.

IDE_RTC ($01cc)

Query the real-time-clock module

IN: -

OUT(s): Fc=1
        BC=date, in MS-DOS format
  DE=time, in MS-DOS format

OUT(f): Fc=0, real-time-clock module not present

Register status on return:
......../.. same
AFBCDEHL/IX different

NOTE:

This call returns the results provided by the RTC.SYS loadable module.
Error codes

The error codes that may be returned by +3DOS/IDEDOS calls are as follows:
Recoverable disk errors:

0	rc_ready	Drive not ready
1	rc_wp	Disk is write protected
2	rc_seek	Seek fail
3	rc_crc	CRC data error
4	rc_nodata	No data
5	rc_mark	Missing address mark
6	rc_unrecog	Unrecognised disk format
7	rc_unknown	Unknown disk error
8	rc_diskchg	Disk changed whilst +3DOS was using it
9	rc_unsuit	Unsuitable media for drive

Non-recoverable errors:

20	rc_badname	Bad filename
21	rc_badparam	Bad parameter
22	rc_nodrive	Drive not found
23	rc_nofile	File not found
24	rc_exists	File already exists
25	rc_eof	End of file
26	rc_diskfull	Disk full
27	rc_dirfull	Directory full
28	rc_ro	Read-only file
29	rc_number	File number not open (or open with wrong access)
30	rc_denied	Access denied
31	rc_norename	Cannot rename between drives
32	rc_extent	Extent missing
33	rc_uncached	Uncached
34	rc_toobig	File too big
35	rc_notboot	Disk not bootable
36	rc_inuse	Drive in use

56	rc_invpartition	Invalid partition
57	rc_partexist	Partition already exists
58	rc_notimp	Not implemented
59	rc_partopen	Partition open
60	rc_nohandle	Out of handles
61	rc_notswap	Not a swap partition
62	rc_mapped	Drive already mapped
63	rc_noxdpb	No XDPB
64	rc_noswap	No suitable swap partition
65	rc_invdevice	Invalid device
67	rc_cmdphase	Command phase error
68	rc_dataphase	Data phase error
69	rc_notdir	Not a directory

The esxDOS-compatible API

The esxDOS-compatible API is a bit simpler to use than the +3DOS-compatible API.

To make a call, you only need to set up the entry parameters as indicated and perform a RST $08; DEFB hook_code. On return, registers AF,BC,DE,HL will all be changed. IX,IY and the alternate registers are never changed (except for M_P3DOS).

(Note that the standard 48K BASIC ROM must be paged in to the bottom of memory, but this is the usual situation after starting a machine code program with a USR function call).

Notice that error codes are different from those returned by +3DOS calls, and also the carry flag is SET for an error condition when returning from an esxDOS call (instead of RESET, as is the case for +3DOS).

If desired, you can use the M_GETERR hook to generate a BASIC error report for any error returned, or even use it to generate your own custom BASIC error report.

All of the calls where a filename is specified will accept long filenames (LFNs) and most will accept wildcards (for an operation such as F_OPEN where a single file is always used, the first matching filename will be used).

Dot commands

Dot commands can also be written using the esxDOS-compatible API. To write such a command, assemble your code to run at origin $2000 (8192), and save the binary file without an extension to the C:/BIN/ directory. (Alternatively, a dot command may be run from any directory by fully-pathing it, or from the Browser by adding a .DOT extension).

When writing dot commands, the entry parameters used for hook codes are slightly different: HL should be used instead of IX. Exit parameters are unchanged.

As well as RST $08 for hook codes, two further restarts may be used:

RST $10
Print the character in A (NOTE: A must not be $80).

RST $18; DEFW address
Call a routine in the standard 48K BASIC ROM.

If a BASIC error occurs during a RST $10 or RST $18 call (eg the user presses BREAK at a “scroll?” prompt) the dot command will be terminated and the error reported, unless you have registered an error handler with the M_ERRH hook.

The maximum code/data size available is 8K. It is permissable to relocate the stack to within the 8K area if desired (except when calling an external ROM with RST $10, RST $18 or the M_P3DOS hook code).

On entry to your dot command, HL contains the address of the arguments following the command name (or 0 if there are no arguments). Additionally, BC contains the address of the entire command line (including the command name but excluding the leading “.”).

The arguments/command line may be terminated by $00, $0d or ':' (since the address usually points within a BASIC statement, but may also be a system-supplied null-terminated line).

If your dot command is >8K in length, only the first 8K is loaded (at $2000), but the file is left open (with the pointer directly after the first 8K). It is possible to obtain the file handle using the M_GETHANDLE hook. This allows you to read further code/data from your dot command into another memory area (perhaps a bank allocated using IDE_BANK via M_P3DOS) or into the standard 8K area as required.

On exit from your dot command, return with the the carry flag reset if execution was successful.

To report a standard esxDOS error, set the carry flag and return with A=error.

To generate a custom error report, set the carry flag and return with A=0 and HL=address of error message (last character must have bit 7 set).

The following calls are available in the esxDOS-compatible API:

; Low-level calls

disk_filemap ; $85 (133)	obtain file allocation map
disk_strmstart ; $86 (134)	start streaming operation
disk_strmend ; $87 (135)	end streaming operation

; Miscellaneous calls.

m_dosversion ; $88 (136)	get NextOS version/mode information
m_getsetdrv ; $89 (137)	get/set default drive
m_tapein ; $8b (139)	tape redirection control (input)
m_tapeout ; $8c (140)	tape redirection control (output)
m_gethandle ; $8d (141)	get handle for current dot command
m_getdate ; $8e (142)	get current date/time
m_execcmd ; $8f (143)	execute a dot command
m_geterr ; $93 (147)	get or generate error message
m_p3dos ; $94 (148)	execute +3DOS/IDEDOS/NextOS call
m_errh ; $95 (149)	register dot command error handler

; File calls.

f_open ; $9a (154)	open file
f_close ; $9b (155)	close file
f_sync ; $9c (156)	sync file changes to disk
f_read ; $9d (157)	read file
f_write ; $9e (158)	write file
f_seek ; $9f (159)	set file position
f_fgetpos ; $a0 (160)	get file position
f_fstat ; $a1 (161)	get open file information
f_ftruncate ; $a2 (162)	truncate/extend open file
f_opendir ; $a3 (163)	open directory for reading
f_readdir ; $a4 (164)	read directory entry
f_telldir ; $a5 (165)	get directory position
f_seekdir ; $a6 (166)	set directory position
f_rewinddir ; $a7 (167)	rewind to start of directory
f_getcwd ; $a8 (168)	get current working directory
f_chdir ; $a9 (169)	change directory
f_mkdir ; $aa (170)	make directory
f_rmdir ; $ab (171)	remove directory
f_stat ; $ac (172)	get unopen file information
f_unlink ; $ad (173)	delete file
f_truncate ; $ae (174)	truncate/extend unopen file
f_chmod ; $af (175)	change file attributes
f_rename ; $b0 (176)	rename/move file
f_getfree ; $b1 (177)	get free space

esxDOS-compatible error codes

Unknown error ; 0, esx_ok
OK ; 1, esx_eok
Nonsense in esxDOS ; 2, esx_nonsense
Statement end error ; 3, esx_estend
Wrong file type ; 4, esx_ewrtype
No such file or dir ; 5, esx_enoent
I/O error ; 6, esx_eio
Invalid filename ; 7, esx_einval
Access denied ; 8, esx_eacces
Drive full ; 9, esx_enospc
Invalid i/o request ; 10, esx_enxio
No such drive ; 11, esx_enodrv
Too many files open ; 12, esx_enfile
Bad file number ; 13, esx_ebadf
No such device ; 14, esx_enodev
File pointer overflow ; 15, esx_eoverflow
Is a directory ; 16, esx_eisdir
Not a directory ; 17, esx_enotdir
Already exists ; 18, esx_eexist
Invalid path ; 19, esx_epath
Missing system ; 20, esx_esys
Path too long ; 21, esx_enametoolong
No such command ; 22, esx_enocmd
In use ; 23, esx_einuse
Read only ; 24, esx_erdonly
Verify failed ; 25, esx_everify
Sys file load error ; 26, esx_eloadingko
Directory in use ; 27, esx_edirinuse
MAPRAM is active ; 28, esx_emapramactive
Drive busy ; 29, esx_edrivebusy
Unknown filesystem ; 30, esx_efsunknown
Device busy ; 31, esx_edevicebusy

; ***************************************************************************
; * DISK_FILEMAP ($85) *
; ***************************************************************************
; Obtain a map of card addresses describing the space occupied by the file.
; Can be called multiple times if buffer is filled, continuing from previous.
; Entry:
; A=file handle (just opened, or following previous DISK_FILEMAP calls)
; IX=buffer
; DE=max entries (each 6 bytes: 4 byte address, 2 byte sector count)
; Exit (success):
; Fc=0
; DE=max entries-number of entries returned
; HL=address in buffer after last entry
; A=card flags: bit 0=card id (0 or 1)
; bit 1=0 for byte addressing, 1 for block addressing
; Exit (failure):
; Fc=1
; A=error
;
; NOTES:
; Each entry may describe an area of the file between 2K and just under 32MB
; in size, depending upon the fragmentation and disk format.
; Please see example application code, stream.asm, for full usage information
; (available separately or at the end of this document).

; ***************************************************************************
; * DISK_STRMSTART ($86) *
; ***************************************************************************
; Start reading from the card in streaming mode.
; Entry: IXDE=card address
; BC=number of 512-byte blocks to stream
; A=card flags
; Exit (success): Fc=0
; B=0 for SD/MMC protocol, 1 for IDE protocol
; C=8-bit data port
; Exit (failure): Fc=1, A=esx_edevicebusy
;
; NOTES:
; On the Next, this call always returns with B=0 (SD/MMC protocol) and C=$EB
; When streaming using the SD/MMC protocol, after every 512 bytes you must read
; a 2-byte CRC value (which can be discarded) and then wait for a $FE value
; indicating that the next block is ready to be read.
; Please see example application code, stream.asm, for full usage information
; (available separately or at the end of this document).

; ***************************************************************************
; * DISK_STRMEND ($87) *
; ***************************************************************************
; Stop current streaming operation.
; Entry: A=card flags
; Exit (success): Fc=0
; Exit (failure): Fc=1, A=esx_edevicebusy
;
; NOTES:
; This call must be made to terminate a streaming operation.
; Please see example application code, stream.asm, for full usage information
; (available separately or at the end of this document).

; ***************************************************************************
; * M_DOSVERSION ($88) *
; ***************************************************************************
; Get API version/mode information.
; Entry:
; -
; Exit:
; For esxDOS <= 0.8.6
; Fc=1, error
; A=14 ("no such device")
;
; For NextOS:
; Fc=0, success
; B='N',C='X' (NextOS signature)
; DE=NextOS version in BCD format: D=major, E=minor version number
; eg for NextOS v1.94, DE=$0194
; HL=A=0 if running in NextOS mode (and zero flag is set)
; HL,A<>0 if running in 48K mode (and zero flag is reset)

; ***************************************************************************
; * M_GETSETDRV ($89) *
; ***************************************************************************
; Get or set the default drive.
; Entry:
; A=0, get the default drive
; A<>0, set the default drive to A
; bits 7..3=drive letter (0=A...15=P)
; bits 2..0=drive number (0)
; Exit (success):
; Fc=0
; A=default drive, encoded as:
; bits 7..3=drive letter (0=A...15=P)
; bits 2..0=drive number (0)
; Exit (failure):
; Fc=1
; A=error code
;
; NOTE:
; This call isn't really very useful, as it is not necessary to provide a
; specific drive to calls which need a drive/filename.
; For such calls, you can instead provide:
; A='*'	use the default drive
; A='$' use the system drive (C:, where the NEXTOS and BIN directories are)

; ***************************************************************************
; * M_TAPEIN ($8b) *
; ***************************************************************************
; Tape input redirection control.
; Entry:
; B=0, in_open:
; Attach tap file with name at IX, drive in A
; B=1, in_close:
; Detach tap file
; B=2, in_info:
; Return attached filename to buffer at IX and drive in A
; B=3, in_setpos:
; Set position of tape pointer to block DE (0=start)
; B=4, in_getpos:
; Get position of tape pointer, in blocks, to HL
; B=5, in_pause:
; Toggles pause delay when loading SCREEN$
; On exit, A=1 if pause now enabled, A=0 if not
; B=6, in_flags:
; Set tape flags to A
; bit 0: 1=pause delay at SCREEN$ (as set by in_pause)
; bit 1: 1=simulate tape loading with border/sound

; ***************************************************************************
; * M_TAPEOUT ($8c) *
; ***************************************************************************
; Tape output redirection control.
; Entry:
; B=0, out_open:
; Create/attach tap file with name at IX for appending, drive A
; B=1, out_close:
; Detach tap file
; B=2, out_info:
; Return attached filename to buffer at IX and drive in A
; B=3, out_trunc:
; Create/overwrite tap file with name at IX, drive A

; ***************************************************************************
; * M_GETHANDLE ($8d) *
; ***************************************************************************
; Get the file handle of the currently running dot command
; Entry:
; -
; Exit:
; A=handle
; Fc=0
;
; NOTES:
; This call allows dot commands which are >8K to read further data direct
; from their own file (for loading into another memory area, or overlaying
; as required into the normal 8K dot command area currently in use).
; On entry to a dot command, the file is left open with the file pointer
; positioned directly after the first 8K.
; This call returns meaningless results if not called from a dot command.

; ***************************************************************************
; * M_GETDATE ($8e) *
; ***************************************************************************
; Get the current date/time.
; Entry:
; -
; Exit:
; Fc=0 if RTC present and providing valid date/time, and:
; BC=date, in MS-DOS format
; DE=time, in MS-DOS format
; Fc=1 if no RTC, or invalid date/time, and:
; BC=0
; DE=0

; ***************************************************************************
; * M_EXECCMD ($8f) *
; ***************************************************************************
; Execute a dot command.
; Entry:
; IX=address of commandline, excluding the leading "."
; terminated with $00 (or $0d, or ':')
; Exit (success):
; Fc=0
; Exit (failure):
; Fc=1
; A=error code (0 means user-defined error)
; HL=address of user-defined error message within dot command
;
; NOTES:
; The dot command name can be fully-pathed if desired. If just a name is
; provided, it is opened from the C:/BIN directory.
; eg: defm "hexdump afile.txt",0 ; runs c:/bin/hexdump
; defm "./mycommand.dot afile.txt",0 ; runs mycommand.dot in current
; ; directory
; If A=0, the dot command has provided its own error message but this is not
; normally accessible. It can be read using the M_GETERR hook.
; This hook cannot be used from within another dot command.

; ***************************************************************************
; * M_GETERR ($93) *
; ***************************************************************************
; Entry:
; A=esxDOS error code, or 0=user defined error from dot command
; if A=0, IX=error message address from dot command
;
; B=0, generate BASIC error report (does not return)
; B=1, return error message to 32-byte buffer at DE
;
; NOTES:
; Dot commands may use this call to fetch a standard esxDOS error message
; (with B=1), but must not use it to generate an error report (with B=0) as
; this would short-circuit the tidy-up code.
; User programs may use the call to generate any custom error message (and not
; just a custom message returned by a dot command). To do this, enter with
; A=0 and IX=address of custom message, where IX>=$4000.
; Custom error messages must be terminated with bit 7 set on the final
; character.

; ***************************************************************************
; * M_P3DOS ($94) *
; ***************************************************************************
; Make a +3DOS/IDEDOS/NextOS API call.
; Entry:
; DE=+3DOS/IDEDOS/NextOS call ID
; C=RAM bank that needs to be paged (usually 7, but 0 for some calls)
; B'C',D'E',H'L',AF,IX contain entry parameters for call
; Exit:
; exit values as described for +3DOS/IDEDOS/NextOS call ID
; EXCEPT: any value to be returned in IX will instead be in H'L'
; All registers except IX,IY may be changed.
;
; NOTES:
; Do not attempt to use this hook code unless you are running in NextOS mode
; (can be determined by using the M_DOSVERSION hook).
; Any parameters which are addresses of data (eg filenames etc) must lie between ; $4000...$BFE0.
; Any errors returned will be +3DOS/IDEDOS/NextOS error codes, not esxDOS error
; codes. Additionally, carry flag RESET indicates an error condition.
; No $DFFD paging should be in force.
; MMU2 ($4000-$5fff) must be the default (lower half of RAM bank 5), containing
; the system variables.
; The stack should be in normal configuration (not in TSTACK).
; For calls requiring normal configuration (ROM2/5/2/0), RAM0 must already
; be paged. For other calls, any banks can be paged at $c000, and will be
; restored when the +3DOS call has completed.

; ***************************************************************************
; * M_ERRH ($95) *
; ***************************************************************************
; Install error handler for dot command.
; Entry: HL=address of error handler within dot command
;	(0 to change back to standard handler)
;
; NOTES:
; Can only be used from within a dot command.
; If any BASIC error occurs during a call to ROM3 (using RST $10 or RST $18)
; then your error handler will be entered with:
; DE=address that would have been returned to if the error had not
; occurred
; A=BASIC error code-1 (eg 8=9 STOP statement)

; ***************************************************************************
; * F_OPEN ($9a) *
; ***************************************************************************
; Open a file.
; Entry:
; A=drive specifier (overridden if filespec includes a drive)
; IX=filespec, null-terminated
; B=access modes, a combination of:
; any/all of:
;	esx_mode_read $01	request read access
;	esx_mode_write $02	request write access
;	esx_mode_use_header $40	read/write +3DOS header
; plus one of:
;	esx_mode_open_exist $00	only open existing file
;	esx_mode_open_creat $08	open existing or create file
;	esx_mode_creat_noexist $04	create new file, error if exists
;	esx_mode_creat_trunc $0c	create new file, delete existing
;
; DE=8-byte buffer with/for +3DOS header data (if specified in mode)
; (NB: filetype will be set to $ff if headerless file was opened)
; Exit (success):
; Fc=0
; A=file handle
; Exit (failure):
; Fc=1
; A=error code

; ***************************************************************************
; * F_CLOSE ($9b) *
; ***************************************************************************
; Close a file or directory.
; Entry:
; A=file handle or directory handle
; Exit (success):
; Fc=0
; A=0
; Exit (failure):
; Fc=1
; A=error code

; ***************************************************************************
; * F_SYNC ($9c) *
; ***************************************************************************
; Sync file changes to disk.
; Entry:
; A=file handle
; Exit (success):
; Fc=0
; Exit (failure):
; Fc=1
; A=error code

; ***************************************************************************
; * F_READ ($9d) *
; ***************************************************************************
; Read bytes from file.
; Entry:
; A=file handle
; IX=address
; BC=bytes to read
; Exit (success):
; Fc=0
; BC=bytes actually read (also in DE)
; HL=address following bytes read
; Exit (failure):
; Fc=1
; BC=bytes actually read
; A=error code
;
; NOTES:
; EOF is not an error, check BC to determine if all bytes requested were read.

; ***************************************************************************
; * F_WRITE ($9e) *
; ***************************************************************************
; Write bytes to file.
; Entry:
; A=file handle
; IX=address
; BC=bytes to write
; Exit (success):
; Fc=0
; BC=bytes actually written
; Exit (failure):
; Fc=1
; BC=bytes actually written

; ***************************************************************************
; * F_SEEK ($9f) *
; ***************************************************************************
; Seek to position in file.
; Entry:
; A=file handle
; BCDE=bytes to seek
; IXL=seek mode:
;	esx_seek_set	$00	set the fileposition to BCDE
;	esx_seek_fwd	$01	add BCDE to the fileposition
;	esx_seek_bwd	$02	subtract BCDE from the fileposition
; Exit (success):
; Fc=0
; BCDE=current position
; Exit (failure):
; Fc=1
; A=error code
;
; NOTES:
; Attempts to seek past beginning/end of file leave BCDE=position=0/filesize
; respectively, with no error.

; ***************************************************************************
; * F_FGETPOS ($a0) *
; ***************************************************************************
; Get current file position.
; Entry:
; A=file handle
; Exit (success):
; Fc=0
; BCDE=current position
; Exit (failure):
; Fc=1
; A=error code

; ***************************************************************************
; * F_FSTAT ($a1) *
; ***************************************************************************
; Get file information/status.
; Entry:
; A=file handle
; IX=11-byte buffer address
; Exit (success):
; Fc=0
; Exit (failure):
; Fc=1
; A=error code
;
; NOTES:
; The following details are returned in the 11-byte buffer:
; +0(1)	'*'
; +1(1)	$81
; +2(1)	file attributes (MS-DOS format)
; +3(2)	timestamp (MS-DOS format)
; +5(2)	datestamp (MS-DOS format)
; +7(4) file size in bytes

; ***************************************************************************
; * F_FTRUNCATE ($a2) *
; ***************************************************************************
; Truncate/extend file.
; Entry:
; A=file handle
; BCDE=new filesize
; Exit (success):
; Fc=0
; Exit (failure):
; Fc=1
; A=error code
;
; NOTES:
; Sets the filesize to precisely BCDE bytes.
; If BCDE<current filesize, the file is trunctated.
; If BCDE>current filesize, the file is extended. The extended part is erased
; with zeroes.
; The file position is unaffected. Therefore, if truncating, make sure to
; set the file position within the file before further writes (otherwise it
; will be extended again).
; +3DOS headers are included as part of the filesize. Truncating such files is
; not recommended.

; ***************************************************************************
; * F_OPENDIR ($a3) *
; ***************************************************************************
; Open directory.
; Entry:
; A=drive specifier (overridden if filespec includes a drive)
; IX=directory, null-terminated
; B=access mode (only esx_mode_use_header and esx_mode_use_lfn matter)
; any/all of:
; esx_mode_use_lfn $10	return long filenames
;	esx_mode_use_header $40	read/write +3DOS headers
; Exit (success):
; A=dir handle
; Fc=0
; Exit (failure):
; Fc=1
; A=error code
;
; NOTES:
; Access modes determine how entries are formatted by F_READDIR.

; ***************************************************************************
; * F_READDIR ($a4) *
; ***************************************************************************
; Read next directory entry.
; Entry:
; A=handle
; IX=buffer
; Exit (success):
; A=number of entries returned (0 or 1)
; If 0, there are no more entries
; Fc=0
; Exit (failure):
; Fc=1
; A=error code
;
; Buffer format:
; 1 byte	file attributes (MSDOS format)
; ? bytes	file/directory name, null-terminated
; 2 bytes	timestamp (MSDOS format)
; 2 bytes	datestamp (MSDOS format)
; 4 bytes file size
;
; NOTES:
; If the directory was opened with the esx_mode_use_lfn bit, long filenames
; (up to 260 bytes plus terminator) are returned; otherwise short filenames
; (up to 12 bytes plus terminator) are returned.
; If opened with the esx_mode_use_header bit, after the normal entry follows the
; 8-byte +3DOS header (for headerless files, type=$ff, other bytes=zero).

; ***************************************************************************
; * F_TELLDIR ($a5) *
; ***************************************************************************
; Get current directory position.
; Entry:
; A=handle
; Exit (success):
; BCDE=current offset in directory
; Fc=0
; Exit (failure):
; Fc=1
; A=error code

; ***************************************************************************
; * F_SEEKDIR ($a6) *
; ***************************************************************************
; Set current directory position.
; Entry:
; A=handle
; BCDE=offset in directory to seek to (as returned by F_TELLDIR)
; Exit (success):
; Fc=0
; Exit (failure):
; Fc=1
; A=error code

; ***************************************************************************
; * F_REWINDDIR ($a7) *
; ***************************************************************************
; Rewind directory position to the start of the directory.
; Entry:
; A=handle
; Exit (success):
; Fc=0
; Exit (failure):
; Fc=1
; A=error code

; ***************************************************************************
; * F_GETCWD ($a8) *
; ***************************************************************************
; Get current working directory.
; Entry:
; A=drive
; IX=buffer for null-terminated path
; Exit (success):
; Fc=0
; Exit (failure):
; Fc=1
; A=error code

; ***************************************************************************
; * F_CHDIR ($a9) *
; ***************************************************************************
; Change directory.
; Entry:
; A=drive specifier (overridden if filespec includes a drive)
; IX=path, null-terminated
; Exit (success):
; Fc=0
; Exit (failure):
; Fc=1
; A=error code

; ***************************************************************************
; * F_MKDIR ($aa) *
; ***************************************************************************
; Create directory.
; Entry:
; A=drive specifier (overridden if filespec includes a drive)
; IX=path, null-terminated
; Exit (success):
; Fc=0
; Exit (failure):
; Fc=1
; A=error code

; ***************************************************************************
; * F_RMDIR ($ab) *
; ***************************************************************************
; Remove directory.
; Entry:
; A=drive specifier (overridden if filespec includes a drive)
; IX=path, null-terminated
; Exit (success):
; Fc=0
; Exit (failure):
; Fc=1
; A=error code

; ***************************************************************************
; * F_STAT ($ac) *
; ***************************************************************************
; Get unopened file information/status.
; Entry:
; A=drive specifier (overridden if filespec includes a drive)
; IX=filespec, null-terminated
; DE=11-byte buffer address
; Exit (success):
; Fc=0
; Exit (failure):
; Fc=1
; A=error code
;
; NOTES:
; The following details are returned in the 11-byte buffer:
; +0(1)	drive specifier
; +1(1)	$81
; +2(1)	file attributes (MS-DOS format)
; +3(2)	timestamp (MS-DOS format)
; +5(2)	datestamp (MS-DOS format)
; +7(4) file size in bytes

; ***************************************************************************
; * F_UNLINK ($ad) *
; ***************************************************************************
; Delete file.
; Entry:
; A=drive specifier (overridden if filespec includes a drive)
; IX=filespec, null-terminated
; Exit (success):
; Fc=0
; Exit (failure):
; Fc=1
; A=error code

; ***************************************************************************
; * F_TRUNCATE ($ae) *
; ***************************************************************************
; Truncate/extend unopened file.
; Entry:
; A=drive specifier (overridden if filespec includes a drive)
; IX=source filespec, null-terminated
; BCDE=new filesize
; Exit (success):
; Fc=0
; Exit (failure):
; Fc=1
; A=error code
;
; NOTES:
; Sets the filesize to precisely BCDE bytes.
; If BCDE<current filesize, the file is trunctated.
; If BCDE>current filesize, the file is extended. The extended part is erased
; with zeroes.
; +3DOS headers are included as part of the filesize. Truncating such files is
; not recommended.

; ***************************************************************************
; * F_CHMOD ($af) *
; ***************************************************************************
; Modify file attributes.
; Entry:
; A=drive specifier (overridden if filespec includes a drive)
; IX=filespec, null-terminated
; B=attribute values bitmap
; C=bitmap of attributes to change (1=change, 0=do not change)
;
; Bitmasks for B and C are any combination of:
;	A_WRITE	%00000001
;	A_READ	%10000000
;	A_RDWR	%10000001
;	A_HIDDEN	%00000010
;	A_SYSTEM	%00000100
;	A_ARCH	%00100000
;
; Exit (success):
; Fc=0
; Exit (failure):
; Fc=1
; A=error code

; ***************************************************************************
; * F_RENAME ($b0) *
; ***************************************************************************
; Rename or move a file.
; Entry:
; A=drive specifier (overridden if filespec includes a drive)
; IX=source filespec, null-terminated
; DE=destination filespec, null-terminated
; Exit (success):
; Fc=0
; Exit (failure):
; Fc=1
; A=error code

; ***************************************************************************
; * F_GETFREE ($b1) *
; ***************************************************************************
; Gets free space on drive.
; Entry:
; A=drive specifier
; Exit (success):
; Fc=0
; BCDE=number of 512-byte blocks free on drive
; Exit (failure):
; Fc=1
; A=error code

Streaming API example - stream.asm

; ***************************************************************************
; * Streaming file access example code for NextOS via esxDOS API *
; ***************************************************************************
; Assemble with: pasmo stream.asm stream.bin
;
; Execute with stream.bin and test.scr (any 6912-byte headerless screen file)
; in the same directory, using:
;
; CLEAR 32767:LOAD "stream.bin" CODE 32768
; LET x=USR 32768
;
; PRINT x to show any esxDOS error code on return.
; Additionally, 255 means "out of data"
; and 65535 means "completed successfully".

; ***************************************************************************
; * esxDOS API and other definitions required *
; ***************************************************************************

; Calls
f_open equ $9a ; opens a file
f_close equ $9b ; closes a file
disk_filemap equ $85 ; obtains map of file data
disk_strmstart equ $86 ; begin streaming operation
disk_strmend equ $87 ; end streaming operation

; File access modes
esx_mode_read equ $01 ; read access
esx_mode_open_exist equ $00 ; open existing files only

; Next registers
next_register_select equ $243b
nxr_peripheral2 equ $06

; Size of filemap buffer (in 6-byte entries)
; To guarantee all entries will fit in the filemap at once, allow 1 entry for
; every 2K of filesize. The example uses a 6.75K SCREEN$, so 4 entries is
; sufficient.
; (NOTE: Reducing this to 1 *may* force the example code to refill the filemap
; multiple times, but only if your card has a cluster size of 2K or 4K
; and the file is fragmented).
filemap_size equ 4

; ***************************************************************************
; * Initialisation *
; ***************************************************************************

        org $8000

; Before starting we will disable the Multiface button, since filesystem
; access will not be possible during a streaming operation, and could cause
; unexpected effects, including possibly the machine locking up until a soft
; reset is performed.

        ld bc,next_register_select
        ld a,nxr_peripheral2
        out (c),a
        inc b
        in a,(c) ; get current peripheral2 value
        and %11110111 ; clear bit 3 (multiface enable)
        out (c),a

; First the file must be opened in the normal way

        ld a,'*' ; use default drive if none specified
        ld ix,test_filename
        ld b,esx_mode_read+esx_mode_open_exist
        rst $08
        defb f_open
        jp c,exit_with_error
        ld (filehandle),a ; store the returned file handle

; For this example, we are going to "stream" a standard Spectrum SCREEN$
; file to the screen. This is a convenient point to set up parameters
; for this.

        ld hl,$4000 ; address to stream data to
        ld de,6912 ; size of data left to stream
        exx ; save in alternate registers

; ***************************************************************************
; * Filemap buffer setup *
; ***************************************************************************

; Next, obtain the map of card addresses for the file.
; Note that this call (DISK_FILEMAP) must be made directly after opening the
; file - no other file access calls should be made first.
;
; A buffer must be provided to hold the card addresses.
;
; Each entry in the buffer occupies 6 bytes and describes an area of the
; file which can be anywhere between 2K and 32MB in size (depending on the
; way the card was formatted, and how fragmented the file is).
; Therefore, it is possible to calculate the absolute maximum number of buffer
; entries required by dividing the size of the file by 2K.
;
; It is also possible to use a smaller buffer and call disk_filemap multiple
; times when a refill is required (provided the last streaming operation has
; been stopped before the next disk_filemap call is made).
;
; Often, files are unfragmented, and so will use only 1 entry. You could
; potentially write your code to assume this (which would therefore be simpler
; than this example), and cause an error if more than 1 entry is returned,
; citing "framentation" and suggesting the user run the .defrag dot command
; on the file. (Note that some CompactFlash, and other IDE, may be limited
; to a maximum section size of 64K).
;
; The byte/block addressing flag returned in bit 1 of A may be useful if you
; wish to start streaming data from a particular 512-byte block offset within
; the file, as it indicates how to adjust the 4-byte card addresses:
; if bit 1 of A=0, then add 512 to the card address for every block
; if bit 1 of A=1, then add 1 to the card address for every block

refill_map:
        ld a,(filehandle)
        ld ix,filemap_buffer ; address of buffer
        ld de,filemap_size ; size of buffer (in 6-byte entries)
        rst $08
        defb disk_filemap
        jp c,close_and_exit_with_error

; On exit from disk_filemap, the return values are:
; DE=size of buffer unused (in 6-byte entries)
; HL=address in buffer after last written entry
; A=flags: bit 0=card id (0 or 1)
; bit 1=0 for byte addressing, 1 for block addressing

        ld (cardflags),a ; store card flags for later use

; First we will check whether there were any entries returned, and exit with
; a dummy error code ($ff) not used by esxDOS to indicate "out of data" if not.

        push hl
        ld de,filemap_buffer ; initialise buffer address
; and a ; not needed as no error, so carry=0
        sbc hl,de ; any entries in the buffer at all?
        pop hl
        ld a,$ff ; dummy error to indicate out of data
        jr z,close_and_exit_with_error

; ***************************************************************************
; * Main streaming loop *
; ***************************************************************************
; Now we can enter a loop to stream data from each entry in the buffer.

stream_loop:
        push hl ; save buffer end address
        ex de,hl ; HL=address of next entry in buffer
        ld e,(hl)
        inc hl
        ld d,(hl)
        inc hl
        ld c,(hl)
        inc hl
        ld b,(hl) ; BCDE=card address
        inc hl
        push bc
        pop ix ; IXDE=card address
        ld c,(hl)
        inc hl
        ld b,(hl) ; BC=number of 512-byte blocks
        inc hl
        push hl ; save updated buffer address
        push bc ; save number of blocks

; Streaming is initiated by calling DISK_STRMSTART with:
; IXDE=card address
; BC=number of 512-byte blocks to stream
; A=card flags, as returned by DISK_FILEMAP
; After this call is issued it is important that no further esxDOS calls
; (or NextOS calls which might access a filesystem) are issued until the
; matching DISK_STRMEND call has been made.
; It is also important to ensure that the Multiface (which could access files)
; is disabled for the duration of the streaming operation. (Done earlier in
; this example).

        ld a,(cardflags) ; A=card flags
        rst $8
        defb disk_strmstart
        pop ix ; retrieve number of blocks to IX
        jr c,drop2_close_and_exit_with_error

; If successful, the call returns with:
; B=protocol: 0=SD/MMC, 1=IDE
; C=data port
; NOTE: On the Next, these values will always be:
; B=0
; C=$EB
; Therefore, your code code be slightly faster and simpler if writing a
; Next-only program. However, these values are provided to allow portable
; streaming code to be written (if NextOS is later ported to other platforms).

        ld a,c
        exx ; switch back to "streaming set"
        ; HL=address, DE=bytes to stream
        ld c,a ; C=data port

; ***************************************************************************
; * Block streaming loop *
; ***************************************************************************

stream_block_loop:
        ld b,0 ; prepare for 256-byte INIR

        ld a,d
        cp 2 ; at least 1 block to stream?
        jr c,stream_partial_block

; Read an entire 512-byte block of data.
; These could be unrolled to INIs for maximum performance.

        inir ; read 512 bytes from the port
        inir
        dec d ; update byte count
        dec d

; Check the protocol being used.
        exx
        ld a,b ; A=protocol (0=SD/MMC, 1=IDE)
        exx
        and a ; The IDE protocol doesn't need
        jr nz,protocol_ide ; this end-of-block processing

; For SD protocol we must next skip the 2-byte CRC for the block just read.
; Note that maximum performance of the interface is 16T per byte, so nops
; must be added if not using INI/OUTI.
; The interface can run at CPU speeds of at least 21MHz (as in ZX-Badaloc).

        in a,(c)
        nop
        in a,(c)
        nop

; And then wait for a token of $FE, signifying the start of the next block.
; A value of $FF indicates "token not yet available". Any other value is an
; error.

wait_token:
        in a,(c) ; wait for start of next block
        cp $ff ; (a token is != $ff)
        jr z,wait_token
        cp $fe ; the correct data token is $fe
        jr nz,token_error ; anything else is an error

; IDE protocol streaming can rejoin here.
protocol_ide:
        ld a,d ; check if any more bytes needed
        or e
        jr z,streaming_complete

        dec ix ; decrement block count
        ld a,ixl
        or ixh
        jr nz,stream_block_loop ; continue until all blocks streamed

        exx ; switch "streaming set" to alternates

; ***************************************************************************
; * Main streaming loop end *
; ***************************************************************************
; After all the 512-byte blocks for a particular card address have been
; streamed, the DISK_STRMEND call must be made. This just requires A=cardflags.

        ld a,(cardflags)
        rst $08
        defb disk_strmend
        jr c,drop2_close_and_exit_with_error

; Following disk_strmend, the system is back in a state where any other esxdos
; calls may now be used, including (if necessary) DISK_FILEMAP to refill the
; buffer. This can be an expensive call, though, so it would be preferable to
; ensure that the buffer is large enough to be filled with the first call.
; This would also simplify the code a little.

        pop de ; DE=current buffer address
        pop hl ; HL=ending buffer address
; and a ; not needed; carry=0 since no error
        sbc hl,de ; any more entries left in buffer?
        jr z,refill_map ; if not, refill
        add hl,de ; re-form ending address
        jr stream_loop ; back for next entry in the buffer

; ***************************************************************************
; * Stream a partial block *
; ***************************************************************************
; It is entirely okay to stream a partial block, since the streaming operation
; can be terminated at any point by issuing the DISK_STRMEND call.

stream_partial_block:
        and a ; at least 256 bytes left?
        jr z,stream_final_bytes

        inir ; read 256 bytes from the port

stream_final_bytes:
        ld b,e
        inc b
        dec b
        jr z,streaming_complete

        inir ; read last few bytes from the port

streaming_complete:
        ld a,(cardflags)
        rst $08
        defb disk_strmend ; terminate the streaming operation
        jr drop2_close_and_exit_with_error

; ***************************************************************************
; * Tidy up and exit *
; ***************************************************************************

token_error:
        ld a,$ff ; dummy error to indicate out of data
        scf

drop2_close_and_exit_with_error:
        pop hl ; discard buffer addresses
        pop hl

close_and_exit_with_error:
        push af ; save error status

        ld a,(filehandle)
        rst $08
        defb f_close

        pop af ; restore error status

exit_with_error:
        ld hl,$2758
        exx ; BASIC requires H'L'=$2758 on return
        ld b,0
        ld c,a ; BC=error, for return to BASIC
        ret c ; exit if there was an error
        ld bc,$ffff ; use 65535 to indicate "no error"
        ret

; ***************************************************************************
; * Data *
; ***************************************************************************

test_filename:
        defm "test.scr",0 ; filenames must be null-terminated

filehandle:
        defb 0

filemap_buffer:
        defs filemap_size*6 ; allocate 6 bytes per entry

cardflags:
        defb 0

List of updates

Updates: 18 Jan 2018
Added more information about dot commands.

Added M_GETHANDLE, M_EXECCMD and M_GETERR hooks.

Updates: 17 Jan 2018
Added note about turning off layer 2 writes.

Added note about layer 2 banks in IDE_BANK call.

Updates: 15 Jan 2018
Added general descriptions of the +3DOS-compatible and esxDOS-compatible APIs.

Added full documentation for the esxDOS-compatible API.

Updates: 12 Dec 2017
Updated details of the IDE_GET_LFN call. This now additionally returns the file's size and last update time & date.

Added new IDE_RTC call for querying the real-time-clock (if present).

Updates: 30 Nov 2017
Updated details of the IDE_BROWSER call. This now has a capabilities mask allowing selected functionality to be enabled or disabled as desired. Also added note about using as a save file dialog.

Updates: 23 Nov 2017
The IDE_STREAM_LINEIN call has been removed and replaced by a new IDE_WINDOW_LINEIN call.

Added new IDE_INTEGER_VAR call for accessing NextBASIC integer variables.

Noted that the IDE_STREAM_* calls may corrupt the alternate register set, in addition to the effects on the standard register set noted for each individual call. (The special note about memory configuration has also been removed for the IDE_WINDOW_* calls; this applies only to the IDE_STREAM_* calls).

Updates: 14 Nov 2017
Added note that it is now possible to use the wildcard character * in the IDE_BROWSER call to match remaining characters in the filetype (with examples).

Added more notes on the IDE_STREAM_LINEIN call.

Added new IDE_WINDOW_STRING call.